## Slide 1
Introduction to cubesat development

## Slide 2
The cubesat concept – timeline and statistics
The on board computer (OBC)
  The OBC missions
  The microcontroller unit (MCU)
  The PC104 standard
The satellite software
  The satellite state machine
  The operating system
  Software layers
Outline (Part A)

## Slide 3
Part 1: The cubesat concept

## Slide 4
The cubesat standard
“ The purpose of the project is to provide a standard for design of picosatellites to reduce cost and development time, increase accessibility to space, and sustain frequent launches”
From the cubesat design specification document: http://www.cubesat.org/resources/
Notes: First: define standard
Second: Accessibility,

## Slide 5
1999
2003
2013
2017
Introduced by groups in Caltech and Stanford
Turning point in cubesat commercial use
First cubesat successful launch
Constellations:
QB50 scientific flock 2k –commercial
Exponential growth of cubesat launches, research and development
The cubesat concept – timeline
Notes: First intended for educational reasons for students, same capabitlites of the sputnik
Up to 2013 most cubesats were used for academic purposes

## Slide 6
Launches per year
Taken from the cubesat & nanosats database: www.nanosats.eu
Notes: Nanosatellites – up to 10kg
2.

## Slide 7
Launches per organizations
Taken from the cubesat & nanosats database: www.nanosats.eu

## Slide 8
Taken from the cubesat & nanosats database: www.nanosats.eu
Taken from the cubesat & nanosats database: www.nanosats.eu
Launches per country
Notes: Wikipedia – first satellites for many countries, mention UNOOSA

## Slide 9
The cubesat failure rate
Taken from Langer & Boumeester (2016) “Reliability of cubesats, statistical data, developers’ belief and the way forward”

## Slide 10
Taken from https://sites.google.com/a/slu.edu/swartwout/
The cubesat failure rate

## Slide 11
The cubesat concept – main lessons
Test and retest.
Avoid non standard HW as much as possible
Use only parts with flight heritage
Make the design Simple and then simplify
Stay focused on mission!

## Slide 12
Part 2: the on board computer

## Slide 13
Areas of interest – cubesat R&D
Notes: Cubesat – multidisciplinary project

## Slide 14
OBC software missions
OBC
1
2
3
4
5
Payload
EPS
COM
Electric power system
Control loop over battery voltage.
Check temperature and currents in range.
Communication systems
Receive commands from GS
Build packets and Send data from SAT to GS
Manage activation of payload
Retrieve data from payload
ADCS
Antennas
Payload
Antennas
Attitude determination and control
Receive estimates of attitude and angular rates
Switch between ADCS modes when necessary
Retrieve ADCS parameters
Deploy antennas.

## Slide 15
Additional missions
Run main state machine of satellite.
Manage memory
Configure inter-satellite communication
Update software
Etc.

## Slide 16
Divide and conquer
1. Main logic
2. EPS
3. Communication
. 4. ADCS
5. Payload

## Slide 17
OBC - the micro-controller unit (MCU)
Definition: A microcontroller is a single chip containing at least a CPU, non-volatile memory, volatile memory, a timer and an I/O control unit.
Notes: Basically a computer on chip
Volatile memory is computer memory that requires an active power connection to function

## Slide 18
MCUs are everywhere!!
An Arduino MCU
Notes: Statistics: Around 60 MCU’s in a regular household

## Slide 19
Advantages of MCU
Low power consumption.
Powerful and carefully chosen electronics systems – resulting in low prices.
Prior knowledge is hardly needed for programming.
Notes: All these make it a perfect match for nanosatellites!!

## Slide 20
The MCU structure

## Slide 21: The MCU timing module

## Slide 22: The MCU interrupt module
Notes: First explain what is the idea behind interrupts, why does it adher to MCU power.

## Slide 23: Interrupt code example – Duchifat 1

## Slide 24: The MCU I2C communication module
Clock
Data
OBC (master)
EPS (slave)
COM (slave)

## Slide 25: I2C read/write functions
void I2C_write(int length, int sa ,char *srcadr)
void I2C_read(int length, int sa , char *dstadr)

## Slide 26: Back to OBC – Cubesat PC104 standard
Taken from the Clyde space EPS user manual (used in Duchifat 1)

## Slide 27
Part 3: The cubesat software components

## Slide 28: Cubesat software layers
Satellite main logic and tasks
Drivers for cubesat components
Operating system
Low level MCU (HAL)

## Slide 29: Examples for low level MCU functions
void I2C_write(int length, int sa ,char *srcadr)
void I2C_read(int length, int sa , char *dstadr)
void init_timer();

## Slide 30: Operating system
Definition: An operating system (OS) is a collection of software that manages computer hardware resources and provides common services for computer programs.

## Slide 31: Operating system
Important functions: memory management, processor management, security etc.
Advantages for cubesats:
Allows for better modularity between the different cubesat assignments. Each assignment is run as a separate thread.
Better failure tolerance.
Notes: Additional advantages, separation between different projects

## Slide 32: Definition of SW thread
A thread is a path of execution through the program.
Notes: Example of book reading

## Slide 33: OS – code example (Duchifat 2)
Notes: Add second example of dump thread

## Slide 34: Driver example
From the ISIS TRXUV user manual

## Slide 35: Main logic - the cubesat state machine